## Slide 1: SLAM Map Comparison Study Between Slam Toolbox and Cartographer
MOTIVATION
  The TurtleBot 3 platform with ROS2 offers an ideal setup for testing and comparing modern SLAM algorithms. However, implementations such as Cartographer and SLAM Toolbox can generate maps of varying quality even under identical conditions.
  This study is motivated by the need to evaluate and quantify these differences to determine which algorithm produces more consistent, geometrically accurate maps in both simulation and real-world environments. Understanding these variations will help improve future autonomous navigation projects that rely on precise localization and mapping.
  By improving SLAM accuracy and reliability, we move closer to solving challenges such as loop closure, where a robot correctly recognizes and aligns previously visited areas.
Stenneth Swaby
Department of Computer Science, The College of New Jersey
Mentor: Dr. Sejong Yoon
RESULTS
Table Comparing Our established ground truths and the map dimensions from Cartographer and SLAM Toolbox.
  Calculating the error in mapping area
    Absolute Error = ∣Mapped−Ground Truth∣
    Percent Error = (Error / Ground Truth) ×100
  Slam Toolbox
    The maze area error was 0.47%, showing high accuracy in large-scale mapping.
  Cartographer
    Boxes 1 and 2 errors were moderate (24% and 20%, respectively), suggesting shape distortion around smaller features.
    Boxes 3 and 4 had higher deviations (35% and 50%), indicating rounding of edges and less geometric accuracy for compact structures.
  SLAM Toolbox achieved a more accurate overall representation of the maze environment, with an average percent error of approximately 9%, compared to 27% for Cartographer. This performance difference reflects SLAM Toolbox’s superior geometric precision, particularly during LiDAR scans around Boxes 2 and 4, where object boundaries and corner geometries were more sharply preserved. In contrast, Cartographer generated a visually continuous and cohesive map with smoother transitions and fewer discontinuities, but it exhibited a tendency to overestimate smaller structural regions, as indicated by the higher percentage errors in Boxes 3 and 4.These results suggest that while Cartographer prioritizes global smoothness and visual uniformity, SLAM Toolbox demonstrates greater fidelity in local structural reconstruction and spatial accuracy.
METHODOLOGY
  The goal of this experiment was to evaluate and compare the mapping accuracy, reliability, and consistency of two SLAM algorithms, Cartographer and SLAM Toolbox, using a controlled test environment.
  SLAM ToolBox map
  Cartographer map
  To minimize experimental error and ensure the collection of accurate, real-world data, a rectangular path was outlined within the maze to serve as a fixed route for the TurtleBot 3. This setup allowed the robot to follow a consistent trajectory during each trial, reducing variability between runs. The robot was manually controlled by the operator using the teleop program, ensuring that its movements remained steady and repeatable while the SLAM algorithms captured LiDAR data. This approach provided a controlled environment for generating reliable mapping results and improved the overall precision of the comparison between Cartographer and SLAM Toolbox.
  To successfully launch and operate both SLAM systems, several ROS2 packages and nodes were required to coordinate sensor data, motion control, and map visualization. The turtlebot3_bringup package was first launched to initialize the robot’s sensors, motors, and LiDAR scanner, providing access to essential topics such as /scan, /odom, and /cmd_vel.
  The turtlebot3_description package supplied the robot’s URDF model, ensuring that sensor placement and frame transformations were accurately represented during mapping.
  For SLAM Toolbox, the slam_toolbox_bringup package was used to start the main SLAM node responsible for real-time scan matching and pose graph optimization.
  Cartographer relied on the cartographer_ros and cartographer_bringup packages to initialize its 2D SLAM node and occupancy grid conversion node, which together built and visualized the map.
  RViz 2 served as the visualization tool, allowing live observation of LiDAR data and the evolving occupancy grid maps. Together, these packages and nodes enabled the TurtleBot 3 to navigate, collect sensor data, and generate comparable maps for both SLAM algorithms under identical experimental conditions.
BACKGROUND/PRIOR WORKS
  Over the summer, I expanded on this research by experimenting with another SLAM framework known as TinySLAM. During this phase, I conducted additional mapping tests and used Python’s Matplotlib library to visualize the LiDAR sensor data collected from the robot. This helped me better understand how different SLAM algorithms interpret spatial information and generate maps in real time.
DISCUSSION
The comparative analysis between Cartographer and SLAM Toolbox revealed that while both algorithms are capable of generating consistent maps, their approaches to spatial reconstruction differ in accuracy and structure. SLAM Toolbox demonstrated stronger local precision, capturing sharper edges and more geometrically accurate outlines of smaller features such as Boxes 2 and 4. This finding suggests that its pose-graph optimization technique provides higher fidelity in local scan alignment, especially when LiDAR reflections occur at short ranges.
Cartographer, on the other hand, produced smoother and more visually continuous maps. However, this global consistency came at the cost of over-generalizing small structures, resulting in larger percent errors for compact features. The algorithm’s scan-matching and loop-closure heuristics emphasize global map cohesion, which can cause rounding effects in confined spaces.
In conclusion, every effort was made to minimize experimental error during data collection. The maze was hand-constructed, and the robot was manually guided along a fixed path marked with painter’s tape to maintain consistent distance from the walls during mapping. While small variations in driving precision and manual measurement may have introduced minor errors in the recorded dimensions, these discrepancies were minimal compared to the clear performance differences observed between the two SLAM algorithms.
REFERENCES
ROBOTIS. (n.d.). TurtleBot3 quick start guide. ROBOTIS e-Manual. Retrieved November 2, 2025, from https://emanual.robotis.com/docs/en/platform/turtlebot3/quick-start/
Articulated Robotics. (n.d.). Getting ready to build a ROS robot. Retrieved November 2, 2025, from https://articulatedrobotics.xyz/category/getting-ready-to-build-a-ros-robot
PROBLEM FORMULATION
The primary problem addressed in this project is determining which SLAM (Simultaneous Localization and Mapping) algorithm Cartographer or SLAM Toolbox produces more accurate and consistent maps under identical conditions. Both algorithms are widely used for autonomous navigation but often yield different results depending on factors such as sensor noise environment environment geometry. These variations can directly affect a robot’s ability to localize itself and navigate efficiently. Therefore, this study formulates the problem as a comparative analysis of mapping accuracy, reliability, and structural consistency between the two SLAM systems. By using a controlled maze environment with fixed ground-truth measurements, the experiment aims to quantify the deviations between generated maps and real-world dimensions, ultimately identifying which algorithm provides more precise geometric representation and better overall performance for TurtleBot 3 applications.
Feature | Ground Truth Area | Cartographer Area | % Error | Slam Toolbox Area | % Error
Maze | 3.344m2 | 3.675m2 | 9% | 3.36m2 | 0.47%
Box 1 | 0.1865m2 | 0.14m2 | 24% | 0.18m2 | 3.5%
Box 2 | 0.1865m2 | 0.225m2 | 20% | 0.18m2 | 3.5%
Box 3 | 0.1073m2 | 0.135m2 | 35% | 0.124m2 | 15%
Box 4 | 0.07m2 | 0.105m2 | 50% | 0.0875m2 | 25%